## Slide 1: Streamline: A Fast, Flushless Cache Covert-Channel Attack by Enabling Asynchronous Collusion
Gururaj Saileshwar1,
Christopher Fletcher2, Moinuddin Qureshi1
ASPLOS-2021
1
2
3x -6x higher bit-rate vs state-of-the-art covert-channel attacks
Note: The authors reserve all rights to this presentation. Fair use for educational purposes is permissible.

## Slide 2: What are Covert-Channels? Why Important?
Trojan
Spy
Sandbox
Core-1
Core-0
Last-Level Cache (LLC)
1, 0, 1 ..
Hit, Miss, Hit ..
Cache Covert-Channel [Perceival’05]:
Trojan transmits bits covertly to Spy via Cache Contention
Importance of Bit-rate: Determines Payload Size & Transmission Time

## Slide 3: State-of-the-art Covert-Channels
CORE-0
(Trojan)
CORE-1
(Spy)
B
LLC
Shared Address
(Read-only)
Flush
1
Load  ‘1’,
No-Load  ‘0’
2
Reload:
Hit/Miss  ‘1’ / ‘0’
3
Flush+Reload Attack [USENIX-SEC’14]
Wait & Repeat
Wait & Repeat
1. Synchronous Operation
Bit-rate limited to < 500KB/s
2. Applicable to certain ISAs (x86) Requires unprivileged usage of Cacheline Flush Instruction (clflush)
Q. Real Upper Bound on Bit-rate for Cache Covert-Channels?
Q. How to make these Universally Applicable to all ISAs?
Limitations:

## Slide 4: Goal: Fast and Universal Covert-Channel
Key Idea of Streamline Attack – Make it Asynchronous and Flushless!
LLC
Sender
Shared Array
Larger than LLC
Asynchronous
FIFO-like Operation
Cache-Thrashing Evicts Previous Lines
Benefits
Fast: Bit-rate depends only on
load execution-rate
Does not require explicit flushes: Applicable to all ISAs
However, Asynchronous Channels Face Many Challenges
For Low Error-Rates!
Receiver
R
S
Load  ‘1’,
No-Load  ‘0’
LLC-Hit  ‘1’,
LLC-Miss  ‘0’

## Slide 5: Challenges for Asynchronous Channels
LLC
LLC
S
2. Fooling
Prefetcher
3. Fooling Replacement-Policy
S
1. Rate-Matching
Sender & Receiver
LLC
R
S
Challenges for Streamline & All Future Asynchronous Channels
Prefetched
Evicted by
Replacement policy

## Slide 6: Contribution-1: Rate-Matching Sender & Receiver
Rate-Matching
LLC
R
S
Remove Payload-Dependent Rate-Variation
with PRNG Channel-Encoding
Tx-i = Payload-i ^ PRNG-i;
Payload-i = Rx-i ^ PRNG-i;
2. Match Sender & Receiver Operations
Add timer instruction (rdtscp) to Sender & throttle its rate to match the Receiver
3. Coarse-Grain Synchronization Every 200K bits (using any Covert-Channel)
PRNG-Modulation
+ Coarse-Grain Sync
+ Throttling Sender
Sender
Receiver
LLC-Miss 1 LLC-Hit
LLC-Miss 1 LLC-Hit
Skipped 0 LLC-Miss
Skipped 0 LLC-Miss
Bit

## Slide 7: Contributions-2,3: Fooling Prefetcher, Repl-Policy
LLC
Prefetcher
S
Fooling
Prefetcher
Fooling Replacement-Policy
Stride of 3 across 2 pages
LLC
2x
2x
2x
2x
Re-access LLC addresses
to update reuse bits
Repl-Policy
S

## Slide 8: Results - Streamline Bit-Rate and Error-Rate
Bit-rate 1800 KB/s
Bit-error-rate 0.4%
Attack | Bit-Rate | Error-Rate
Streamline (LLC) | 1800 KB/s | 0.4%
Flush-Flush (LLC)1 | 496 KB/s | 0.8%
Flush-Reload (LLC)1 | 298 KB/s | <0.1%
Take-a-Way (L1)2 | 588 KB/s | 1 - 3%
Prime-Probe (L1)3 | 400 KB/s | Not evaluated
1. [DIMVA’16], 2. [ASIACCS’20], 3. [BSDCan’05]
Takeaways: 1. Fastest Cache Covert-Channel (3x vs FlushFlush, 6x vs FlushReload)
2. Flush-less  applicable to all CPUs/ISAs.
Results on Intel Xeon E3-1270 (Skylake)
(Also tested on i5/i7, Kaby-Lake/Coffee-Lake)
Comparisons with Prior Attacks

## Slide 9: Results – Resilience to Noise
Streamline error-rate under noise from co-running applications (Stress-NG Benchmarks)
(averaged over 5 runs)
Sync-Period - 50,000 bits
0.8%
At Smaller Synchronization Periods, Streamline uses smaller sized FIFOs in LLC to buffer bits and achieves Noise Resilience
Sync-Period - 200,000 bits
15%

## Slide 10: Mitigation Strategy
Restricting usage of flush instructions as a defense (SHARP-ISCA’17, ARM-ISA) does not prevent Streamline
Noise injection as a defense provides limited protection, as Streamline can be made noise-resilient
Detection based defenses (e.g. using Perf-Counters) also is limited in applicability: False positives and negatives
Disabling Shared Memory or Partitioning Shared Caches (e.g. DAWG-MICRO’18) fully mitigates Streamline

## Slide 11: Limitation: New Bottleneck in Covert Channels
Measurement Bottleneck: Fundamentally Limits Bit-Rate of Streamline & Future Attacks
Inability to Execute & Measure Latency of Multiple Loads in Parallel
Overcoming this bottleneck and measuring load-latency of multiple loads in parallel, can unlock ~10x increase in bitrate of covert-channel
rdtscp //read timer
load x
rdtscp //read timer
Using rdtscp [Intel SW Developer’s Manual]
Serialized due to Fence-like semantics of rdtscp
Using Counting-Thread [DIMVA’17]
Thread-0
load ctr
load x
load ctr
--------
load ctr
load y
load ctr
Thread-1
while(1){
ctr++;
}
Serialized due to
TSO ordering in Intel CPUs
--------
rdtscp //read timer
load y
rdtscp //read timer

## Slide 12: Conclusion
Streamline is flushless attack with broad applicability (all uarch, ISA)
Covert-channel bit-rate 3x-6x higher than prior attacks
  Eliminates Synchronization Bottleneck in prior attacks
Measurement bottleneck limits all future attacks
  Addressing this can considerably increase bit-rates
Trojan
Sender
Spy
Receiver
Processor Cache
R
S
Streamline Attack