## Slide 1: SYNERGY: Rethinking Secure-Memory Design for Error-Correcting Memories
Gururaj Saileshwar1
HPCA-2018
Vienna, Austria
Prashant Nair1
Prakash Ramrakhyani2
Wendy Elsasser2
Moinuddin Qureshi1
1
2

## Slide 2: Designing Resilient Memories for Servers
Security
Reliability
Server memories need protection against data corruption
Attack Resilience – Memory Security
by Natural Errors
Resilient Memories
Error Resilience – ECC-DIMM
ECC
SGX
(Software Guard Extensions)
SYNERGY
Co-Design of
Security-Reliability
Better Performance – 20%
Better Reliability – 185X
Maintaining Security
No Extra Storage
by Malicious Attacks
Security
Reliability
Co-Design

## Slide 3: Threat Model for Memory Modules
Unauthorized Reads
Unauthorized Writes
Replay Attack
Man-in-the-middle Attack
Secure memory needs to protect against these attacks !
Cold Boot Attack
DMA Attack
Cores
Cache
System
Memory

## Slide 4: How Do Secure Memories Work ?
Data
Counters
Secure Root On-Chip
Signatures
Unauthorized Reads
Unauthorized Writes
Replay Attack
Counter Mode Encryption
Encrypted Data
Data
Message Authentication Code
Cryptographic
Hash
Integrity-Tree
Intel SGX
Data
Counter Mode Encryption
Counter
Counter-Based
Signature / MAC
Message Authentication Code
Integrity-Tree
+1

## Slide 5: Problem: Metadata Accesses Consume Memory Bandwidth
1
3
2
4
.
.
.
Data Cacheline
MAC Cacheline
MAC
Encryption Counter Cacheline
Ctr
Integrity-Tree Counter Cacheline
Ctr
Prevents Replay-Attacks
Used to Encrypt Data
Memory Access Bloat
Memory Access Bloat due to Security Metadata can lead to Performance Overheads
Cacheable On-Chip
Prevents Data Tampering
Access Number
Secure Memory can require 4+ memory accesses for each Data access

## Slide 6: Dissecting Overheads For Secure Memory
Chart: Normalized Performance
| SGX_O | Non-Secure
Performance | 1 | 2.1
Cause: Memory access bloat due
to metadata accesses
Chart: Memory Accesses / Data
| SGX_O
Data | 1
Counters | 0.46512
MACs | 0.86047
SGX_O – Enhanced Baseline for Secure Memory
(SGX with LLC shared by Counters & Data)
Counters
MACs
Data
2X Gap
Performance - Secure vs Non-Secure Memory
Goal:
Reduce MAC access bloat to improve secure memory performance
MACs cause 0.9x additional accesses – focus of this paper !

## Slide 7: Insight: Leverage ECC-DIMM To Reduce MAC Overheads
DATA
ECC
ECC-DIMM for Reliability
MAC
Security with MAC
ECC
ECC
ECC
Fetched
Same Access as Data
Separate Access
MAC
Detects
2-Bit Errors
Any Modifications
Co-Design
1-Bit Error
Corrects
Still need ECC for Correction!
Rare
Replace

## Slide 8: Agenda
Introduction & Background
Synergy Design
Evaluation

## Slide 9: SYNERGY Co-locates MAC & Data for Performance
DATA
ECC
Data Cachelines
MAC
ECC
MAC Cachelines
MAC
MAC
MAC
MAC
MAC
MAC
MAC
Non-Secure
Secure Memory
SYNERGY
MAC
ECC
ECC
ECC
ECC
ECC
ECC
ECC
ECC
ECC
1 access for reads
Synergy avoids extra MAC lookups and improves performance,
without any additional storage
, unless error (rare)
2 accesses for writes
ECC Cachelines
- 1 access
- 2 accesses

## Slide 10: SYNERGY uses MAC for Error Detection
MAC
ECC Cachelines – for correction
DATA
Data + MAC Cachelines
ECC
ECC
ECC
ECC
ECC
ECC
ECC
ECC
ECC
ECC
Can We Achieve Stronger Error-Correction with Co-Design?
ERROR
MISMATCH
HASH
MATCH
MACs have strong error detection ability
Baseline ECC (SECDED) provides
single-bit error correction

## Slide 11: Parity Can Reconstruct Chip With Failure
MAC
ECC Cachelines – for correction
DATA
Data + MAC Cachelines
ECC
ECC
ECC
ECC
ECC
ECC
ECC
ECC
ECC
ECC
D0
D1
D2
D3
D4
D5
D6
D7
P
ECC
P
P
P
P
P
P
P
P
FAILURE









CHIP-WISE PARITY
Parity Can Correct Large-Granularity Failures,
If Chip With Failure Known
How to identify chip with failure?

## Slide 12: SYNERGY uses MAC + Parity for Error Correction
MAC
MAC
DATA
MATCH
MISMATCH
HASH
MAC can detect when
data cacheline is free from error
?
?
Synergy can tolerate 1 chip with failure out of 9 chips, much stronger reliability than SECDED (Baseline)
PARITY









Try & reconstruct each chip till MAC matches!
How to identify chip with failure?
PARITY
Try
Try
Try

## Slide 13: Tolerating Errors in Other Metadata
Data Cacheline
MAC
Encryption Counters Cacheline
Ctr
Integrity-Tree Counters Cacheline
Ctr
Parity Cacheline
P
Errors can occur in any metadata stored in memory
PP
PC
PT
SYNERGY stores Parity with
each metadata to correct errors
Level-wise Error Correction
Algorithm

## Slide 14: Agenda
Introduction & Background
Synergy Design
Evaluation

## Slide 15: Benefit-1: Reduced Memory Traffic
SYNERGY Reduces Metadata Accesses by 36%
Chart: Memory Accesses / Data Access
| SGX_O | SYNERGY | SGX_O | SYNERGY | SGX_O | SYNERGY
Data | 1 | 1 | 1 | 1 | 1 | 1
Counters | 0.38462 | 0.38462 | 0.75 | 0.77778 | 0.48837 | 0.46512
MACs | 0.53846 | 0 | 1.8214 | 0 | 0.86047 | 0
Parity | 0 | 0 | 0 | 1.8148 | 0 | 0.44186
Reads
Writes
Overall
56% ↓
36% ↓
~

## Slide 16: Benefit-2: Better Performance
Chart: Normalized Performance
| SPEC | MIX | GAP | ALL-29
SYNERGY | 1.205 | 1.288 | 1.114 | 1.202
SYNERGY improves performance of secure memory by 20%,
without any additional storage
Performance of SYNERGY normalized to SGX_O

## Slide 17: Benefit-3: Stronger Reliability
Probability of System Failure
(Log Scale)
Years
185X
4X
SYNERGY tolerates 1 chip failure out of 9 chips
Chipkill tolerates 1 chip failure out of 18 chips
SECDED only tolerates single-bit errors
SYNERGY has 185x higher reliability than Baseline ECC-DIMM
Synergy (9 chips x 2 ranks)
Chipkill (18 chips x 1 ranks)
SGX_O – SECDED (9 chip x 2 ranks)

## Slide 18: Conclusion
SYNERGY improves Performance by 20% and Reliability by 185x
Security (MAC)
Reliability (ECC)
Co-Design
Synergy (MAC + Parity)

## Slide 19: Thanks and Questions
“The whole is greater than the sum of its parts” - Aristotle
Synergy