## Slide 1
Moinuddin K. Qureshi
ECE, Georgia Tech
ISCA 2012
Michele Franceschini, Ashish Jagmohan, Luis Lastras
IBM T. J. Watson Research Center
PreSET: Improving PCM performance
by exploiting asymmetry in write times

## Slide 2
In Memoriam
John P. Karidis (1958-2012)
IBM Distinguished Engineer
Initiator & Tech Lead of PCM Project at IBM
Exceptionally Versatile Researcher
Butterfly Laptop Design (now in MOMA/NYC)
Worlds fastest robotic probing arm
PCM: material, devices, architecture, OS
Great Human Being, Mentor, Colleague

## Slide 3: Outline
The Slow-Write Problem
PreSET: Exploiting Write Asymmetry
Experimental Results
Discussion and Summary
Notes: Give a brief overview of the presentation. Describe the major focus of the presentation and why it is important.
Introduce each of the major topics.
To provide a road map for the audience, you can repeat this Overview slide throughout the presentation, highlighting the particular topic you will discuss next.

## Slide 4
Challenges for PCM Memories
DRAM scaling is challenging  PCM promises better scaling
Key Challenges with PCM:
Limited Endurance (10-100M writes/cell)
  - Wear Leveling, Error correction, Graceful degradation
High Read Latency (2X-4X of DRAM)
  -Hybrid Memory, combining PCM and DRAM
High Write Latency (4X-8X higher than PCM read)
Write performance remains one of the key bottleneck for PCM
PCM
$
DRAM
Cache
Hybrid Memory

## Slide 5
Problem: Contention from Slow Writes
Typical response: Writes not latency critical, use buffers/scheduling
Once write gets scheduled, later arriving read request to bank waits
Contention from slow writes increase read latency, lowers performance
WR
RD0
RD0
WR
RD1
RD1
Wait
WR
RD0
RD0
WR
RD1
RD1
WR (redone)
Our previous solution: Adaptive Write Cancellation [HPCA’10]

## Slide 6
Slow Write Problem: Quantified
Baseline: 256MB DRAM$ + 32 PCM banks each with 32-entry WRQ
PCM read latency 500 cycles, write latency 4000 cycles
Our Goal: Get performance close to “No Writes”, without large WRQ
Baseline
AWC
No Writes
Effective Read Latency
Chart: 
 | 1 | 1.211 | 1.388
Speedup
Baseline
AWC
No Writes
Chart: 
 | 982 | 694 | 567

## Slide 7: Outline
The Slow-Write Problem
PreSET: Exploiting Write Asymmetry
Experimental Results
Discussion and Summary
Notes: Give a brief overview of the presentation. Describe the major focus of the presentation and why it is important.
Introduce each of the major topics.
To provide a road map for the audience, you can repeat this Overview slide throughout the presentation, highlighting the particular topic you will discuss next.

## Slide 8
Not All Writes are Created Equal
Writes are slow only in one direction
For typical PCM, write transitions have widely different latencies
SET: Long Latency (~8x of read) RESET: Low Latency (similar to read)
SET
RESET
time
Power

## Slide 9
Insight: Exploit Write Asymmetry
PreSET: Slow operation off-the-critical-path
Typical memory operation writes many bits (512)  Both transitions
If memory writes constrained to only RESET, writes as fast as read
Our Proposal: PreSET (Do SET operations off-the-critical path)
With PreSET, the write only does RESET operations  Low Latency
0xFADEDACE
0xDEADBEEF
0xFADEDACE
0x00000000
0xDEADBEEF
PreSET

## Slide 10
When to do PreSET?
Initiating PreSET at 1st write to line in DRAM$  large PreSET window
As soon as the line is read  Data corruption (if no write)
When the write reaches memory system  Too late
Solution: When line gets first write in DRAM$, initiate PreSET
DRAM$ Install
writes
PreSET Window
Eviction to memory

## Slide 11
Architecture Support for PreSET
PreSET requires small changes, PSQ is much simpler than WRQ
PCM memory arrays needs to support bimodal writes: short and long
Scheduling: PreSET are low priority, non-blocking for read requests
DRAM $
To Processor
PCM
Memory
WRQ
RDQ
PSQ
WR
RD
PreSET (Address only)
V
D
TAG
DATA
PI
PD
PI= PreSET Initiated
PD= PreSET Done

## Slide 12
Working of PreSET
DRAM $
To Processor
PCM
WRQ
RDQ
PSQ
WR
RD
PreSET (Address only)
V
D
TAG
PI
PD
PI=1
PD=1

## Slide 13: Outline
The Slow-Write Problem
PreSET: Exploiting Write Asymmetry
Experimental Results
Discussion and Summary
Notes: Give a brief overview of the presentation. Describe the major focus of the presentation and why it is important.
Introduce each of the major topics.
To provide a road map for the audience, you can repeat this Overview slide throughout the presentation, highlighting the particular topic you will discuss next.

## Slide 14
Read Latency and Speedup
Effective Read Latency
Chart: 
 | 982 | 694 | 661 | 594 | 567
Chart: 
 | 1 | 1.211 | 1.278 | 1.347 | 1.388
Speedup
PreSET is more effective than AWC
PreSET+AWC obtains performance very close to No Writes
Baseline
AWC
PreSET
PreSET+AWC
No Writes
35%

## Slide 15
Impact on Write Queue Size
Chart: 
NoWrites | 1.388 | 1.388 | 1.388 | 1.388 | 1.388 | 1.388
AWC | 1.054 | 1.107 | 1.211 | 1.278 | 1.319 | 1.34
PreSET+AWC | 1.307 | 1.323 | 1.347 | 1.362 | 1.37 | 1.375
Baseline | 0.941 | 0.959 | 1 | 1.014 | 1.017 | 1.017
8
Speedup
Baseline
AWC
PreSET+AWC
8
16
32
64
128
256
AWC is reliant on having large WRQ, but (PreSET+AWC) is not
Number of Entries in WRQ (per bank, 32 banks)
No Writes
1K Entries Total
(32KB)
(64KB)
(128KB)
(256KB)
(512KB)
(1MB)

## Slide 16
Where do the cycles go?
PreSET increases memory utilization  Power/Lifetime overheads
Static/Dynamic throttling schemes for reduce overheads (in paper)

## Slide 17
Chart: 
 | 0.91 | 0.77 | 0.76
Chart: 
 | 1.33 | 1.26 | 1.38
Power and Energy-Delay-Product
Normalized Power
Normalized EDP
AWC
PreSET
PreSET+AWC
PreSET based schemes increase power but improve EDP significantly
-24%

## Slide 18
Lifetime Impact
Lifetime Depends on Write Traffic Utilization (PreSET uses idle cycles)
Our workloads

## Slide 19
Chart: 
 | 4 | 20 | 13.6 | 8.2 | 7.9 | 12.2 | 7.4 | 5 | 4.9
Lifetime Impact
PreSET based schemes have lifetime of 5+ years, higher than rated
Rated
Average Lifetime
Worst-Workload Lifetime
System Lifetime (in Years)
Baseline
AWC
PreSET
PreSET+AWC

## Slide 20: Outline
The Slow-Write Problem
PreSET: Exploiting Write Asymmetry
Experimental Results
Discussion and Summary
Notes: Give a brief overview of the presentation. Describe the major focus of the presentation and why it is important.
Introduce each of the major topics.
To provide a road map for the audience, you can repeat this Overview slide throughout the presentation, highlighting the particular topic you will discuss next.

## Slide 21
Isn’t PreSET Similar to Flash ERASE?
Yes: Both exploit asymmetry in write operations
No:
PreSET is optional, ERASE mandatory
PreSET at same granularity as write, ERASE at 64x-128x
PreSET is “in-place”, ERASE “out-of-place”
PreSET is optional and obviates the (bulky) indirection tables of ERASE
  Limited “out-of-place” PreSET for latency-critical writes: (database-commit, persistent memory, power failure)
  Out-of-place writes  indirection tables (area, latency)
  For PCM, table needs to be per-line (~10MB for 32GB)

## Slide 22
Summary
PCM “Slow-Write” problem: Write blocks read, causes slowdown
We exploit asymmetry in PCM writes: SET is slow, RESET is fast
We propose PreSET, which performs SET ahead of actual write
Starting PreSET on first-write on DRAM$ write is effective
PreSET improves performance by 35% (No-Writes: 39%)
Unlike AWC, PreSET does not rely on large WRQ
(In paper: PreSET throttling for reduced overheads)

## Slide 23
Questions

## Slide 24
Sensitivity to Banks

## Slide 25
Power Breakdown

## Slide 26
SET to RESET Ratio