## Slide 1
Poulami Das*
Swamit Tannu#
Siddharth Dangwal+
Moinuddin Qureshi*
*
#
+
ADAPT: Mitigating Idling Errors in Qubits
via Adaptive Dynamical Decoupling
MICRO-54
Notes: Hi everyone, I am Poulami from Georgia Tech. I am advised by Prof. Moin Qureshi.
Today I will talk about how idle qubits are susceptible to errors and discuss our solutions to mitigate these errors in quantum programs.
This work was done in collaboration with Swamit from University of Wisconsin Madison and Siddharth from IIT Delhi.

## Slide 2
To make quantum computers useful, the application fidelity must be improved
Near-term quantum hardware suffers from high error rates resulting in low program fidelity
Quantum Bits
Error
Quantum Computer
Near-term Quantum Computers are Noisy
Notes: Quantum computers promise computational advantages for many important scientific and commercial applications.
Unfortunately, qubits are prone to hardware errors (click) that result in incorrect outputs. (pause) To make quantum computers useful we must mitigate the impact of hardware errors and improve application fidelity.

## Slide 3
Prior Work on Noise-Aware Compilation
Tannu et al., Murali et al.
CNOT Crosstalk Error!
Crosstalk Aware Compilation
Reduce crosstalk Modulate concurrency
Quantum
Program
Quantum Computer
Map more work on reliable qubits
Variability Aware Compilation
High error
Low error
Notes: Researchers are developing various software techniques for mitigating the impact of hardware errors.
For example, qubits on real quantum hardware such as IBM or Google Quantum computer exhibit variability in error-rates which means some qubits have higher error-rates compared to others.
Prior works show that by mapping more work on the more reliable qubits and avoiding qubits with higher error rates, we can significantly improve the program fidelity.
<click> Moreover, current quantum computers have operational crosstalk. For example, performing concurrent two-qubit gates can increase their effective error rate due the crosstalk. We can reduce this crosstalk by serializing some parts of the quantum program.

## Slide 4
The Problem: Idling Errors
On-going operations significantly increase the idling errors
Qubits encounter errors while performing operations: Active Errors
Error!
Error!
Decoherence
Crosstalk increases idling errors by 10x
Qubits are vulnerable to errors even while they are idle: Idling Errors
Time = 0
Time = t (100 µS)
1
0
1
0
Problem: Idling Errors
Notes: Generally, we talk about active errors where qubits encounter errors while performing operations: for example, gate and measurement errors
<click> But qubits can also encounter errors while they are idle- these are called idling errors.
For example qubits naturally lose information even if they are sitting idle due to <click> Decoherence
For instance qubit devices on IBM quantum hardware only retain their information for few micro-seconds.
<click> Moreover, we observe that active CNOT operations nearby idle qubits generate crosstalk <click> which makes the idle qubits 10 times more vulnerable to errors
<click> Thus, crosstalk from on-going two qubit operations such as cnot can make idling errors significantly worse and degrade program fidelity.

## Slide 5
Idling Errors at the Application-Level
Idle qubits are common, and idling errors reduce the program fidelity
Long-latency of two-qubit operations
Data-dependencies
35ns
idle
2400 ns
Chart: Bernstein Vazirani Circuit Size
| 4 | 6 | 8 | 10 | 12 | 14 | 16 | 18 | 20
 | 2.4178 | 4.4302 | 6.3289 | 8.1707 | 10.3822 | 12.3947 | 14.2791 | 16.5191 | 18.2044 | 19.9253 | 21.7031 | 23.3529 | 25.0738 | 26.9227 | 28.8007 | 29.9804 | 31.4311
SWAP
operations
Notes: So why do we care about idling errors at the application-level?
First, two-qubit gates incur long latencies
And data dependencies cause program qubits to remain idle while operations are being performed.
Lastly, Near-term quantum hardware offer limited connectivity. <click> To overcome this limitation, compilers relocate or SWAP qubits which causes further serialization and <click> large idle time periods
Further, the idle times increase with the program size
<click> So idle qubits are common and idling errors can significantly reduce the program fidelity

## Slide 6
Dynamical Decoupling: Mitigate Idling Errors
Dynamical decoupling can reduce idling errors by keeping idle qubits busy
Dynamical Decoupling (DD): Keep idle qubits busy
Specific gate sequence: X-X or X-Y-X-Y
Effectively Identity gate: Qubit state remains unchanged
Notes: Dynamical decoupling or DD is a populat circuit level technique that can reduce idling errors and is widely used in qubit characterization experiments.
<click> DD applies a specific sequence of single qubit gates for example XX gates and XYXY gates
<click> By applying DD, the qubit does not remain idle anymore. Also, these gates effectively behave as an identity gate and thus, the qubit state remains unchanged.
<click> Thus, DD can reduce idling errors by keeping the idle qubits busy

## Slide 7
Dynamical Decoupling: The Good and Bad
Always applying DD pulses to idle qubits may adversely impact the fidelity
700 qubit-link combinations on IBMQ-Toronto
Best-Case: 3.95x
Worst-Case: 0.21x
Notes: But is DD always helpful? While DD can reduce idling errors, it introduces additional gate operations that can fail.
So we perform more extensive characterization on several IBM quantum devices. The figure here shows the distribution of the fidelity of an idle qubit when DD is used for 700 qubit and active link combinations on IBMQ-Toronto. We observe that although it is generally effective, sometimes it can hurt because the additional operations used to apply DD can introduce errors. For example, in the best case Fidelity improves by up-to 4x compared to no DD whereas in other cases it drops up-to 0.21x.
This happens because the additional gates introduced by the DD pulses can cause errors. If these errors are higher than idling errors, DD does not benefit overall.
<click> Therefore, applying DD pulses always may adversely impact the fidelity and instead we need a robust mechanism to apply DD depending on the benefit.

## Slide 8
Fidelity improves the most when DD is applied to only a subset of qubits
No-DD
DD-for-All
Best Sequence: 010100
DD
DD
DD
DD
DD
DD
Dynamical Decoupling at the Application-Level
Notes: So what does it mean at the application-level. For example, let us take 6-qubit program. We have various options on which qubits to apply DD. For example, we may not apply DD at all. <click> Or we can only apply DD to only two of the qubits. <click> Or we can apply DD to all the qubits.
So for this 6-qubit program we have 2^6 possibilities for applying DD. <click> So we took two 6-qubit programs to understand what happens? <click> Here 0 means no DD whereas <click> 63 means DD on all qubits
<click> We observe that for QFT-6, Best sequence is not really all ones but 010100 which means <click> we must apply DD only to qubits q1 and q3 and <click> not on the remaining qubits
We make similar observation for BV-6 too
<click> Thus, the highest fidelity is only when DD is selectively applied only to a subset of qubits.

## Slide 9
Outline
Background and Motivation
ADAPT: Insights and Design
Evaluation Methodology and Results
Notes: So the natural question is how do we know which qubits to apply DD to? Our proposed solution ADAPT enables us to do so by applying DD in a robust manner.

## Slide 10
Challenges
Goal: Apply DD only to qubits that benefit
Challenge-1: Which qubits will benefit from DD? Hard to characterize all possibilities
0
1
Challenge-2: Do not know correct output.
Thus, can't test fidelity with DD sequences
DD
DD
2
3
4
5
Don’t know
which is better
Notes: Our goal is to apply DD only to qubits that benefit from it, but we don’t know which are these qubits.
The first challenge is that we cannot characterize because there exists an exponential number of all possibilities. For example, consider this 6-qubit quantum computer. On this machine if you perform CNOT between qubits 2 and 3, <click> the crosstalk causes idling errors to increase on qubit 0. On the other hand, Cnot on qubits 4 and 5 does not affect the idling errors. However, concurrent CNOTs on qubits 2-3, and qubits 4-5 increases the idling errors on qubit 1 but not on qubit-0. Thus, idling errors are hard to characterize, <click> and particularly as system size scales due to an exponential increase in the search space.
<click> So rather than characterizing the device, we can <click> apply different DD sequences to a program and <click> check if applying DD improves the fidelity or <click> worsens it
<Click> However, now the challenge is how do we know if fidelity improves or worsens because we do not know the correct output of the program.

## Slide 11
Key Insights
Insight #1: Crosstalk from CNOT gates is a dominant source of idling errors
Insight #2: Not all quantum circuits are hard to simulate
We propose decoy circuits with identical CNOT gates that are easy to simulate and can capture patterns in idling errors
Notes: We use two key insights in ADAPT.
First, Cnot gates are a dominant source of Idling errors at the application-level
Second, Not all circuits are hard to simulate– for example, Clifford gate circuits can be simulated efficiently on conventional machines.
So we propose (1) decoy circuits with cnot structure same as the program that are easy to simulate and use these decoy circuits to capture patterns in idling errors and learn about the optimal subset of qubits to apply DD.

## Slide 12
ADAPT: Design Overview
ADAPT learns the optimal DD sequence for each program
Can be simulated
to find noiseless output
Notes: To find the optimal DD sequence, our proposed design adapt, (1) creates a decoy circuit with identical two qubit gates but where the non-Clifford gates are replaced by the Clifford gates. <click>This circuit can be simulated to find the noiseless output.
<click> Now we apply different DD sequences <click> on this Decoy circuit <click> and <click> execute them on the NISQ device.
<click> Then by computing the fidelity of the output, we identify the optimal DD sequence.
<click> Finally, we apply the optimal DD sequence <click> to the original circuit
<click> Thus, by using decoy circuits ADAPT learns the optimal subset of qubits to apply DD.

## Slide 13
Designing Decoy Circuits
ADAPT uses seeded decoy circuits that keeping the simulation time tractable
Input Program
Trivial Decoy Circuit
Clifford Decoy Circuit
Seeded Decoy Circuit
All-Zero output
Extreme Entropy
Rich state Evolution
H
H
H
Notes: The overall effectiveness of ADAPT depends on the learning from the decoy circuits. So how do we design efficient decoy circuits?
The easiest way to design a decoy circuit is to remove all the single qubit gates and only keep the two-qubit gates. <click> However, this circuit produces all 0 output and is not sensitive to idling errors because this circuit cannot capture phase errors.
Another way to design a Decoy circuit is by <click> replacing all the single qubit gates by only Clifford gates. While this is better than the trivial decoy circuit, we must be careful with it because it may be insensitive to idling errors <click> if the circuit produces a uniform distribution with large entropy
<click> To overcome these challenges, we propose a seeded decoy circuit that keeps a limited number of non-Clifford gates in the initial layer of the circuit and <click> replaces the remaining non-Clifford gates with Clifford gates. <click> This produces a rich state evolution and makes the circuit sensitive to idling errors.
<click> By using seeded decoy circuits, ADAPT can learn about the optimal DD sequence while simultaneously keeping the simulation time tracatable.

## Slide 14
ADAPT: Local Search for Efficiency
The local search algorithm is efficient and makes ADAPT scalable
210 = 1024
Decoy Circuits
Not Scalable
DD
DD
DD
DD
DD
...
16 Decoy Circuits
DD
DD
DD
DD
DD
...
Best: 0101
16 Decoy Circuits
Best: 1101
DD
DD
DD
...
4 Decoy Circuits
Best: 01
Total Decoy Circuits: 36
Optimal Sequence: 0101110101
Notes: Now let us consider a 10 qubit circuit. If we want to find the optimal DD sequence using exhaustive search, <click> we need 2^10 that is 1024 decoy circuits. <click> This exponential scaling is not sustainable.
Instead, ADAPT uses a local search. For the same 10-qubit program now, ADAPT first tries to learn the optimal DD sequence for the first four qubits. <click> For this four-qubit block, ADAPT uses all possible DD sequences. <click>Thus, we need 16 Decoy Circuits.
<click> Next, it moves to the next block of 4 qubits and <click> repeats the search process <click> in a similar manner.
<click> Then, it proceeds to the remaining 2 qubits. <click> this search requires <click> 4 decoy circuits.
<click> Therefore, ADAPT uses only 36 decoy circuits and <click> determines the optimal DD sequence by combining the results from the individual searches.
<click> This local search makes ADAPT scalable and requires significantly reduced number of evaluations

## Slide 15
Outline
Background and Motivation
ADAPT: Insights and Design
Evaluation Methodology and Results
Notes: I will now talk about the Evaluation Methodology and discuss the Results.

## Slide 16
IBMQ hardware: 16 to 27 qubits
Two different DD protocols: XX and XY4
Evaluation Methodology
Up-to 10 qubit benchmarks executed for 32K Trials
IBM Qiskit Compiler with highest optimization levels
Figure-of-Merit: Fidelity
A higher Fidelity is desirable
Notes: For evaluations, we use three different IBM quantum computers with 16 to 27 qubits and <click> run quantum circuits with up to 10 qubits, where we run each circuit for 32K trials.
<click> We use IBM’s Qiskit compilation tool-chain and the highest optimization levels.
<click> We also evaluate our design with two protocols XX and XY-4 and <click> use Total Variation Distance to measure the program fidelity.
<click> Overall, a higher Fidelity is desirable.

## Slide 17
Results
ADAPT is effective: 1.6x on average (including other machines)
Optimal DD sequence from ADAPT outperforms DD-on-All Qubits
Independent of the DD protocol
Chart: Benchmarks on IBMQ-Toronto (With XX DD Sequence)
| QPEA-5 | BV-7 | QFT-6 | BV-8 | Gmean
All-DD | 1.0102 | 1.1656 | 1.6 | 1.1983 | 1.392
ADAPT | 1.2317 | 1.2409 | 1.8 | 1.4324 | 1.5975
Runtime Best | 1.2317 | 1.3977 | 2 | 1.4324 | 1.789
2.3
2.7
3.3
Notes: The Figure here shows the relative program fidelity normalized to the baseline.
<click> We observe the ADAPT improves the application fidelity by up-to 1.6x on average.
<click> The optimal DD sequence from ADAPT outperforms DD-on-All qubits
<click> Also, we observe that ADAPT is effective for both XX and XYXY DD sequences and therefore, does not depend on the DD protocol

## Slide 18
Conclusion
Qubits encounter errors when they are idle. Idling errors can be mitigated by Dynamical Decoupling (DD)
Applying DD to all idle qubits is often sub-optimal
We present ADAPT: A robust software framework for enabling DD
  Uses decoy circuits to identify qubits that will benefit most from DD
  Relies on efficient local search algorithm to find optimal sequence
Fidelity improves by 1.6x on average across three IBMQ machines
Notes: To conclude,
Qubits can encounter errors even if they are not actively performing any operations but are idle. These idling errors can be mitigated by applying Dynamical decoupling or DD.
<click> However, applying DD to all the idle qubits is often sub-optimal and applying DD only to a subset of qubits is most beneficial.
<click> To enable robust application of DD, we propose ADAPT which uses Decoy circuits to identify the qubits which will benefit most from DD and relies on a local search algorithm to efficiently learn the optimal DD sequence.
<click> Our evaluations show that ADAPT improves the fidelity by 1.6x on average across three different IBM machines

## Slide 19
Thank You!