## Slide 1
Poulami Das*
Swamit Tannu#
Moinuddin Qureshi*
*
#
JigSaw: Boosting Fidelity of NISQ Programs via Measurement Subsetting
Notes: Hi everyone, I am Poulami. I am from Georgia Tech and I am advised by Prof. Moin Qureshi.
In this talk, I will be discussing JigSaw which mitigates the impact of measurement errors in NISQ applications. This work was done in collaboration with Swamit who is currently at the University of Wisconsin, Madison

## Slide 2
Chart: Outcomes
| 00 | 01 | 10 | 11
 | 0 | 0.25 | 0.25 | 0.5
Operated in “Noisy Intermediate Scale Quantum (NISQ)” mode
Quantum Computers are Noisy
Noise determines the overall fidelity of NISQ systems
Near-term quantum computers have high error rates
NISQ Device
11
01
11
10
Output Log
Repeat Trials
Correct
Erroneous
Program
Notes: Near-term quantum computers have very high error-rates because of noise.
<Click> They are operated in the Noisy Intermediate Scale Quantum or “NISQ” mode where computations are performed in the presence of noise
<Click> To run a program on a NISQ devices, it is repeatedly executed for several trials.
<Click> At the end of each trial, all the program qubits are measured, and the bitstring or outcome is logged.
<Click> Finally, the output probability distribution is used to infer the program solution. For example, this is a potential output distribution of a 2-qubit program.
<Click> Now let's say the correct answer of this program is 11. We observe many erroneous outcomes in this distribution as well which are produced as a result of noise.
<Click>Therefore, noise determines the overall fidelity of NISQ systems

## Slide 3
The Problem: Measurement Errors
Measurement errors are dominant sources of errors in large programs
Program
CNOT q0, q1
Measure q0
Measure q1
NISQ Hardware
q0
q1
Chart: Error Rates on 27-qubit IBMQ-Toronto
| Two-Qubit Gate | Measurement
Average | 1.2 | 3.8
Worst-Case | 3.5 | 23.1
Map
Error!
Error!
Each trial measures all program qubits
All measurements must be Error-Free
Notes: To understand how errors impact a program execution, let us take the example of this quantum program and this toy NISQ device
<Click> The compiler maps the program to the hardware and computations are performed.
<Click> The program can encounter errors while performing gate operations. However, even if the computations remain error-free in a program,
<Click> qubit measurements at the end of the program can encounter errors.
<Click> More importantly, measurement errors are dominant sources of errors on most existing NISQ systems
This becomes increasingly challenging for large programs
<Click> because in the current execution model, each trial measures all the program qubits AND
<Click> all these measurement operations must be error-free for the trial to be successful
<Click>Thus, measurement errors can significantly limit the fidelity of large programs

## Slide 4
Measurement crosstalk can increase the effective error-rate
Measurement crosstalk increases with program size
Challenge with Measurements at Scale
Crosstalk
Isolated
Multiple
Chart: MEasureMENT Error Rates on GooglE SYCAMORE
| ISOLATED | MULTIPLE
Average | 6.14 | 7.73
Worst-Case | 11.7 | 20.9
Notes: The other challenge with measurement operations is that their error-rates are not static but increases with the number of measurements due to crosstalk.
<Click> For example, if we measure a qubit in isolation, it has a certain measurement error-rate
<Click> However, if we measure it along with many other qubits ,which is what we typically do in programs,
<Click> there is crosstalk between the measurement operations
<Click> which increases the effective error-rate
<Click> Measurement crosstalk becomes increasingly more challenging as programs increase in size due to the increased number of measurement operations

## Slide 5
Chart: Outcomes (q1q0)
| 00 | 01 | 10 | 11
 | 0 | 0 | 0 | 1
The Insights
Insight: Measure fewer qubits and Reconstruct distribution
Goal: Reduce Measurement Errors
Chart: Outcomes (q0)
| 0 | 1
 | 0 | 1
Chart: Outcomes (q1)
| 0 | 1
 | 0 | 1
Chart: Outcomes (q1q0)
| 00 | 01 | 10 | 11
 | 0 | 0 | 0 | 1
X
Ideal
Are high fidelity Circuits with Partial Measurements alone sufficient?
Notes: Our goal is to reduce measurement errors and the insight is that we can Measure only a subset of qubits (to reduce errors) and then Reconstruct the output distribution.
<click> For example, if we have this two-qubit program
<click> We create two copies of the program where the computations are identical but each copy measures only a single qubit.
<click> Next, we execute them and
<click> try to reproduce the output of the original program.
<click> We observe that the reconstructed output matches what we expect.
<click> Therefore, circuits measuring only a subset of qubits seem to be a good approach. But does it always work?

## Slide 6
The Insights
Need for Correlation
X
Ideal
Chart: Outcomes (q1q0)
| 00 | 01 | 10 | 11
 | 0.5 | 0 | 0 | 0.5
Chart: Outcomes (q1)
| 0 | 1
 | 0.5 | 0.5
Chart: Outcomes (q0)
| 0 | 1
 | 0.5 | 0.5
Chart: Outcomes (q1q0)
| 00 | 01 | 10 | 11
 | 0.25 | 0.25 | 0.25 | 0.25
Ideally, we want both correlation and high fidelity
Notes: Let us now take the example of a two-qubit GHZ program
<click> which produces states 00 and 11 with equal probabilities.
<click> We use a similar approach as earlier where we again prepare two copies of the program. The computations remain same in both copies but we measure only a single qubit in each copy.
<click> We execute these program copies and
<click> then try to reconstruct the output distribution.
<click> We observe that the reconstructed distribution does not match the expected distribution (even in the absence of noise). This happens because quantum programs store and manipulate correlated states and measuring all program qubits helps us capture this correlation. But now, we do not know this global correlation as we only measure a subset of qubits in each program copy.
<click> So high fidelity is not sufficient, ideally, we need both correlation and fidelity

## Slide 7
Outline
Background and Motivation
JigSaw: Insights and Design
Evaluations
Notes: Now I will discuss our proposed approach JigSaw

## Slide 8
Program gives full correlation; CPM gives high fidelity. JigSaw combines both
JigSaw: Design
. . .
Original program
Circuits with Partial Measurements (CPM)
NISQ Device
NISQ Device
Global-Mode
(50% of Trials)
Subset-Mode
(50% of Trials)
Recompile
Recompile
Notes: JigSaw gets us both correlation and fidelity:
First, it runs the entire program and measures all qubits to obtain the correlation.
<click> We call this Global-Mode and 50% of the trials are run in global mode.
<click> Next, JigSaw runs several Circuits with partial measurements or “CPM”. These CPM perform identical computations as the input program but measure only a subset of qubits in each copy. The CPM provide marginal information ONLY about the subset of qubits that are measured with high fidelity.
<click> We call this Subset-Mode and the remaining 50% of the trials are run in this mode.
<click> Also, now that we do fewer measurements, we can recompile the CPM to make those measurements on good qubits with low measurement error rates
<click> Finally, JigSaw combines both using a post-processing approach

## Slide 9
?
CPM updates the global distribution and improves the fidelity
Bayesian Reconstruction in JigSaw
Q2Q1Q0 | Prob.
0 0 0 | 0.15
0 0 1 | 0.05
0 1 0 | 0.1
0 1 1 | 0.05
1 0 0 | 0.15
1 0 1 | 0.2
1 1 0 | 0.1
1 1 1 | 0.2
Q1Q0 | Prob.
0 0 | 0.1
0 1 | 0.1
1 0 | 0.1
1 1 | 0.7
Q2Q1Q0 | Score
0 0 0 | 0.06
0 0 1 | 0.01
0 1 0 | 0.06
0 1 1 | 0.47
1 0 0 | 0.06
1 0 1 | 0.09
1 1 0 | 0.06
1 1 1 | 1.87
Q1Q0
Q2
0
1
Global Mode
Subset Mode
Update Coefficients
00 | 01 | 10 | 11
0.5
0.5
0.2
0.8
0.5
0.5
0.2
0.8
0.06
=
Output
Cannot infer solution
Correct!
Q2Q1Q0 | Prob.
0 0 0 | 0.02
0 0 1 | 0.01
0 1 0 | 0.02
0 1 1 | 0.18
1 0 0 | 0.02
1 0 1 | 0.03
1 1 0 | 0.02
1 1 1 | 0.70
Notes: JigSaw updates the probabilities of the outcomes obtained in the global-mode using the results from subset mode. It uses insights from Bayesian statistics where a probability distribution can be updated if marginal information becomes available later.
For example, here we have the output distribution obtained from global-mode for a 3-qubit program. We also have the marginal distribution obtained by measuring only two qubits (Q1 and Q0) in the subset mode.
<click> To update the probabilities, the post-processing scheme first obtains the update coefficients and then assigns an output score to each outcome in the global dist.. To compute the update coefficients it looks at each outcome in the marginal distribution.
<click> For example, first it looks at 00 and searches for all outcomes in the global distribution where q1q0 is 00.
<click> In this case it corresponds to 000 and 100 (basically when q2 is 0 or 1).
<click> It extracts the probabilities from the global distribution and normalizes them to account for their relative contribution.
<click> Next it computes the score by using the update coefficients and using the probability from the marginal distribution. The subtraction in the denominator accounts for the relative probabilities in the marginal distribution. <click>
<Click>Then it moves on to the next outcome in the marginal distribution which is 01 here and repeats the steps.
<click> And finally to 10 and <click> 11
<click>Finally once all updates are performed, the scores are normalized.
Now let uss look at thow JigSaw improves the application Fidelity. Let us assume the correct output is 111
<click>Earlier, if we just tried to infer the correct answer from the histogram peak, we would not be able to, because both 101 and 111 appears with maximum frequency.
<click> But with JigSaw, we can because the subset mode measures Qubits q1 and q0 with greater accuracy and
<click> when this information is used, the fidelity improves

## Slide 10
JigSaw-M: Multi-Layer JigSaw
Program
. . .
CPM
JigSaw-M uses heterogeneous-sized CPM
Default subset size: 2
. . .
More Unique CPM
Other subset size: 3
Notes: In the default design, we only use CPM that measures two qubits each. The subset size refers to the number of qubits measured in each CPM. The default subset size 2 reduces the impact of measurement errors while still capturing some correlation and keeps the design simple.
<click> We also propose an enhanced design where we use different sized CPMs, we call this Multi-Layer JigSaw or JigSaw-M. It uses CPM of size 2, 3, 4 and so on ... <click>
and we use all these CPM to repair the output distribution obtained from the Global Mode.

## Slide 11
Outline
Background and Motivation
JigSaw: Insights and Design
Evaluations
Notes: Now I will discuss our evaluation methodology and results

## Slide 12
IBMQ hardware: 27 to 65 qubits
Evaluation Methodology
Noise aware compilation, 32K– 256K Trials
Figure-of-Merit 1: Probability of Successful Trial (PST)
PST =
A higher PST and Fidelity is desirable
Figure-of-Merit 2: Fidelity
  Fidelity =
Notes: For our evaluations we use three different quantum computers from IBM
<click> We use a noise aware compiler and perform between 32K to 256K trials depending on the size of the program.
<click> For the Figure of Merit, we use probability of successful trial which is the ratio of the number of trials with the correct output to the total number of trials.
<click> We also use Fidelity. It is a distance-based metric that computes the total variation distance between the output distribution on a NISQ device and the distribution on an error-free machine. This is particularly useful for programs that generate a distribution as an output.
<click> Therefore, a higher PST and Fidelity is desirable.

## Slide 13
Chart: Benchmarks on IBMQ-Toronto
| BV-6 | QAOA-8 (p1) | QAOA-10 (p2) | QAOA-10 (p4) | QAOA-12 (p4) | QAOA-14 (p2) | Ising-10 | GHZ-14 | Graycode-18 | Gmean
EDM | 1.2231 | 0.97481 | 0.99881 | 0.90118 | 0.77652 | 0.8895 | 0.95711 | 0.94485 | 0.95425 | 0.95157
JigSaw | 7.8676 | 2.2261 | 2.1397 | 2.4015 | 2.2059 | 2.9014 | 1.9317 | 1.5653 | 2.7174 | 2.5606
JigSaw-M | 8.4153 | 2.3444 | 2.5123 | 2.9026 | 2.6273 | 4.2112 | 2.158 | 1.7994 | 4.6744 | 3.1307
Results for PST
EDM: Ensemble of Diverse Mappings, Tannu et al., MICRO 2019
Average: 3.1x
Best-Case: 8.4x
Notes: We also compare against a recently proposed technique: Ensemble of Diverse Mappings or EDM. In this approach, the program is run on multiple initial mappings.
Here, we show the improvement in PST normalized to the baseline for different benchmarks on IBM Toronto. On an average, the PST improves by 3.1x whereas in the best case it improves up to 8.4x. We also observe that JigSaw outperforms both the baseline and EDM. Multi-layer JigSaw or JigSaw-M is even more effective.

## Slide 14
Chart: Relative Fidelity (Mean)
| IBMQ-Toronto | IBMQ-Paris | IBMQ-Manhattan
EDM | 0.96 | 1.19 | 0.93
JigSaw | 2.17 | 2.33 | 1.84
JigSaw-M | 2.54 | 2.77 | 2.1
Results for Fidelity
Average
JigSaw: 2.1x
JigSaw-M: 2.5x
Notes: The figure here shows the improvement in Fidelity for three different machines normalized to the baseline.
On an average, the Fidelity improves by 2.1x for JigSaw and even further up to 2.5x for JigSaw-M
We have also studied other metrics and the detailed evaluations can be found in the paper.

## Slide 15
How many CPM do we need?
Chart: Number of Circuits with Partial Measurement (CPM)
| 4 | 12 | 20 | 28 | 36 | 44 | 52 | 60
 | 1.6044 | 1.8616 | 1.9499 | 2.0045 | 2.0364 | 2.0756 | 2.0639 | 2.0838 | 2.099 | 2.1111 | 2.1112 | 2.1174 | 2.1261 | 2.1181 | 2.1325 | 2.1375
Diminishing Returns
QAOA-12 (p4) on IBMQ-Paris
Few unique CPM are sufficient, scale linearly with number of qubits (default)
N-qubit program has NC2 possible CPM of subset size 2
Notes: So in order to be effective, JigSaw relies on information from the CPM and understanding how many CPM is needed is important.
For a program with N qubits, Nchoose2 CPM are possible for the default design where each CPM measures a subset of two qubits.
<click> We ran experiments for a 12-qubit QAOA benchmark on IBM Paris and tried to understand the effectiveness of JigSaw with increasing number of CPM. This figure here shows the mean relative improvement in PST with increasing number of CPM. For a 12-qubit program 64 CPM are possible of size 2.
<click> We observe that after few unique CPM are already used, the improvement in PST saturates because the new CPM does not provide any incremental information
<click> Thus, only few CPM are sufficient for JigSaw to be effective. In our default design, we use CPM that scales with the number of qubits. This ensures that there is high fidelity information from the CPM for every program qubit.

## Slide 16
Impact of Recompilation
Recompiling each CPM enhances the effectiveness of JigSaw
Average: No Recompilation-> 1.9x, With Recompilation-> 2.9x
Chart: Mean Relative PST
| IBMQ-Toronto | IBMQ-Paris | IBMQ-Manhattan
EDM | 0.95157 | 1.1737 | 0.82685
JigSaw (No Recompilation) | 1.8492 | 1.8884 | 1.7922
JigSaw (With Recompilation) | 2.5606 | 2.8717 | 2.3806
Notes: In addition to subsetting, JigSaw gets significant improvement due to recompilation of the CPM
The figure here shows the average improvement in PST normalized to the baseline for three different IBM machines.
JigSaw improves the PST by 1.9x on average without any recompilation. However, with recompilation, it further improves the PST to 2.9x on average.
Thus, recompiling the CPM significantly enhances the performance of JigSaw.

## Slide 17
Scalability Analysis
Complexity is determined by number of unique outcomes
JigSaw does updates only for non-zero outcomes (limited by trials)
The linear complexity makes JigSaw scalable to large machines
Program Size (Num. of Qubits) | JigSaw |  | JigSaw-M | 
 | Memory (GB) | Operations (Billion) | Memory (GB) | Operations (Billion)
100 | 1 | 0.4 | 4 | 1.7
500 | 5 | 2.1 | 20 | 8.4
*Assuming 1 Million trials, and pessimistically each trial yields a unique outcome
Notes: We also study the scalability of JigSaw because poor complexity of the post-processing algorithm can reduce its applicability in large programs.
The complexity of JigSaw is determined by the number of outcomes in the global mode.
<click> As JigSaw only updates outcomes appearing with non-zero probability, it is eventually limited by the number of trials and not by the total number of possibilities
To understand this, let us consider a 100-qubit program. It has 2^100 possible outcomes. Even if we assume that the program produces a uniform distribution where each outcome is observed with equal probability, we will still need a minimum of 2^100 trials to observe these outcomes at least once. This is
impractical.
<click> We estimated the complexity analytically assuming a million trials where each trial pessimistically yields a unique outcome. We observe that the memory requirement is few Gigabytes, and the number of operations is a few billions even for large programs.
<click> This linear complexity of JigSaw makes it scalable to large machines

## Slide 18
Conclusion
Measurement errors limit fidelity of large NISQ programs
JigSaw mitigates impact of measurement errors via subsetting
JigSaw measures:
  All program qubits in 50% of trials
  Subset of qubits in remaining 50% trials
JigSaw uses Bayesian post-processing to combine the results
Fidelity improves by 2.5x to 8.4x on 3 IBMQ machines
Notes: To conclude:
Measurement errors are dominant sources of errors in large NISQ programs and can limit the application fidelity
<click> We propose JigSaw that reduces the impact of measurement errors via subsetting
<click> JigSaw runs the program in two modes: first it runs the entire program and measures all the program qubits for 50% of the trials -> this captures the correlation. For the remaining 50% trials, JigSaw runs multiple copies of the program where each program copy only measures a subset of qubits.
<click> Finally, it combines the two using a Bayesian post-processing scheme
<click> Our evaluations on three different IBM devices show that the fidelity improves by 2.5x on average and up-to 8.4x

## Slide 19
Thank You!