## Slide 1: Bespoke Cache Enclaves: Fine-Grained and Scalable Isolation from Cache Side-Channels via Flexible Set-Partitioning
Gururaj Saileshwar, Sanjay Kariyappa and Moinuddin Qureshi
SEED 2021

## Slide 2: Problem: CPU Cache Side-Channels
Shared LLC helps improve performance,
But timing difference (LLC Hit vs Miss) leads to side-channels!
L1 Cache
L2 Cache
CORE-0
Last Level Cache (LLC)
LLC-Hit  Fast
LLC-Miss to DRAM  Slow
Private
L1 Cache
L2 Cache
CORE-1
Shared
DRAM

## Slide 3: Problem: CPU Cache Side-Channels
L1 Cache
L2 Cache
CORE-0
L1 Cache
L2 Cache
CORE-1
SPY
PROCESS
VICTIM
PROCESS
A
B
Ways
Last Level Cache
Conflict-Based Attacks
Prime+Probe, Evict+Time,
Repl-Policy Attacks
Shared
Cache Set

## Slide 4: Problem: CPU Cache Side-Channels
L1 Cache
L2 Cache
CORE-0
L1 Cache
L2 Cache
CORE-1
SPY
PROCESS
VICTIM
PROCESS
A
B
V
Last Level Cache
Secret-Dependent
B
Conflict-Based Attacks
Prime+Probe, Evict+Time,
Repl-Policy Attacks
Spy Lines Evicted due to Set Conflicts

## Slide 5: Problem: CPU Cache Side-Channels
L1 Cache
L2 Cache
CORE-0
Last Level Cache
L1 Cache
L2 Cache
CORE-1
SPY
PROCESS
VICTIM
PROCESS
B
V
Conflict-Based Attacks
Shared-Memory Attacks
Flush+Reload, Flush+Flush, …
Shared Cache Line
Spy has Cache Hits on
Lines Installed by Victim
Install
Hit

## Slide 6: Problem: CPU Cache Side-Channels
L1 Cache
L2 Cache
CORE-0
Last Level Cache
L1 Cache
L2 Cache
CORE-1
SPY
PROCESS
VICTIM
PROCESS
Conflict-Based Attacks
Shared-Memory Attacks
Cache Occupancy Attack
Website-Fingerprinting
[SEC’20], [SEC’21]
Sharing of Cache Space
Spy Infers Changes in Victim Working Set

## Slide 7: Problem: CPU Cache Side-Channels
L1 Cache
L2 Cache
CORE-0
Last Level Cache
L1 Cache
L2 Cache
CORE-1
SPY
PROCESS
VICTIM
PROCESS
Conflict-Based Attacks
Shared-Memory Attacks
Cache Occupancy Attack
Website-Fingerprinting
[SEC’20], [SEC’21]
Sharing of Cache Space
Spy can Leak Victim Secrets like AES/RSA Keys, User Key-Strokes, Cause Privacy Breaches (fingerprint victim activity)

## Slide 8: Landscape of Secure Cache Defenses
Randomization-Based
Obfuscate Mapping of Lines to Sets
(e.g., CEASER(-s), ScatterCache, MIRAGE)
Incomplete Security
(do not prevent occupancy attacks)
Sets
Line
Install (X)
Rf
Partitioning-Based
Principled Security
Limited Scalability or Practicality
Isolate Cache Usage with Way/Set Partitioning
(e.g., DAWG, MI6)
B
B
Our Focus

## Slide 9: Drawbacks of Existing Partitioning Defenses
Way-Partitioning
Page-Coloring
Catalyst [HPCA’16], DAWG [MICRO’18]
STEALTHMEM [SEC’12], MI6 [MICRO’19]
Domain-Based
Way-Selection
Not Scalable (Number of Domains limited by LLC Associativity)

## Slide 10: Drawbacks of Existing Partitioning Defenses
Way-Partitioning
Page-Coloring
Catalyst [HPCA’16], DAWG [MICRO’18]
STEALTHMEM [SEC’12], MI6 [MICRO’19]
Domain-Based
Way-Selection
Not Scalable (Number of Domains limited by LLC Associativity)
Not Flexible (Requires DRAM and LLC allocations in same ratio)
Implication: Limited Adoption in Real-world SW like Browsers

## Slide 11: Drawbacks of Existing Partitioning Defenses
Way-Partitioning
Page-Coloring
DAWG [MICRO’18]
STEALTHMEM [SEC’12], MI6 [MICRO’19]
Domain-Based
Way-Selection
Not Scalable (Number of Domains limited by LLC Associativity)
Not Flexible (Requires DRAM and LLC allocations in same ratio)
GOAL:
Scalable to
100s of Domains
Flexible Cache Allocations
(Independent of DRAM)
Fine-Grain Allocations
(granularity of few KBs)

## Slide 12: Our Solution: Bespoke Cache Enclaves
Cache Enclaves: Isolated Set Partitions of Arbitrary Size per Security Domain
Fine-Grain: Allocations at “Cluster” Granularity (64 Sets)
Flexible: Size Independent of DRAM allocations
Scalable: 512 Cache Enclaves at a time in LLC
Challenges:
Security: How to only Map Lines of a Domain to its own Cache Enclave?
Performance: How to Uniformly Map Lines within an Arbitrary-Sized Enclave?
Key Insight:
Flexible Dynamic Indexing
Cluster
Dynamic LLC Indexing

## Slide 13: Overview of BCE Design
Allocation of LLC Resources Per Domain at a Cluster (64KB) Granularity
cache_alloc
cache_dealloc
OS/SW decides LLC allocation size, HW manages allocation and indexing
Interface:
Privileged Instructions

## Slide 14: Overview of BCE Design
Allocation of LLC Resources Per Domain at a Cluster (64KB) Granularity
Dynamic LLC Indexing
in Hardware

## Slide 15: Overview of BCE Design
Allocation of LLC Resources Per Domain at a Cluster (64KB) Granularity
Split indexing into (a) LineAddr  LCID and (b) LCID  PCID
LLC Indexing in Hardware
Performance
Security

## Slide 16: Overview of BCE Design
Allocation of LLC Resources Per Domain at a Cluster (64KB) Granularity
Randomizing Hash Maps Line-Address  Logical Cluster (LCID)
Indirection Table Maps Clusters to LLC (LCID  PCID mapping)
LLC Indexing in Hardware
LBH Minimizes
Set-Conflicts
CIM Guarantees Isolation & Security

## Slide 17: Deep-Dive: BCE Indexing
Load-Balancing Hash (LineAddr  LCID)
Multiple Randomizing Hashes: Minimizes Set-Conflicts by Uniformly Mapping LineAddr to Clusters
Cluster Indirection Module (LCID  PCID)
One-to-One Mapping: Isolation Based Security
2 Cycle Constant Latency Lookup (no new side-channel)
Detailed Explanations in the Paper
Minimal Storage Overhead (<2%) for Tables (2KB), 9-bits/tag to support 512 Domains

## Slide 18: Results: Flexibility in LLC Allocation of BCE
Case Study: Benefits of BCE vs DAWG [MICRO’18]
15 Cache Insensitive (PageRank) & 1 Cache Sensitive (Roms) Workloads
Trace based simulation of 16-cores, 32MB LLC with 16 ways
2MB
2MB
1.5MB
1MB
0.5MB
LLC Per PageRank
LLC Per Roms
9.5MB
2MB
2MB
17MB
24.5MB
Increase Roms LLC by Squeezing PageRank LLC
Negligible impact on IPC of PageRank on squeezing its LLC allocation
40% IPC speedup vs DAWG for Roms by increasing its LLC allocation

## Slide 19: Results: Overall Performance
Slowdown for Equal-Partitioning vs Non-Secure Baseline
Trace based simulation of 16-cores, 32MB LLC with 16 ways
DAWG: 2%,
Page-Coloring: 0.4%
BCE: 1.4%
BCE has comparable slowdown (1.4%) as Page-Coloring (0.4%)
while allowing LLC allocation independent of DRAM allocation
Additional evaluations related to LLC Misses, LLC Latency, Storage Overheads in the Paper

## Slide 20: Summary
Cache Partitioning is a principled defense against cache side-channels
Prior Cache Partitioning Defenses are Impractical: Way-Partitioning not Scalable, Page-Coloring not Flexible
Bespoke Cache Enclaves: Flexible Set-Partitions via Dynamic Indexing
  Practicality: Scalable to 512 cache enclaves, Fine-grain (64KB granularity allocation), Cache Allocation Independent of DRAM Allocations
  Best-Case Performance: Upto 40% IPC improvement over DAWG with fine-grain sizing
  Costs: On average, 1.4% slowdown vs non-secure baseline, 1.8% LLC storage overhead